## Slide 1: Starting with Cast3M Thermomechanical calculations available on: http://www-cast3m.cea.fr/index.php?xml=formations
Last changes: march 27 2023
François DI PAOLA

## Slide 2: summary
  Introduction to Cast3M
  Gibiane language
  Tutorial class thermo-mechanical behavior of a structure with a circular cavity
  Complements
  Objects in Gibiane

## Slide 3: Introduction to Cast3M

## Slide 4: What is Cast3M?
  A simulation software
  using the finite element method
  thermal and mechanical analysis of structures and fluids
  Partial differential equations solved thanks to the finite element method
  Complete software: solver, pre-processing and post-processing, visualization, reading/writing data…
  Based on a programming language: Gibiane (objet-oriented)

## Slide 5: Application areas
  Structural mechanics
    Quasi-static (non linear behavior, geometry, boundary conditions)
    Contact/friction, Buckling
    Dynamic (temporal, modal, fluid structure interaction)
    Fracture (XFEM, dynamic propagation, cohesive zones models, …)
  Thermal analysis
    Conduction, convection, radiation, phase transition
  Fluid mechanics
  Metallurgy
  Magneto-statics
  Multi species diffusion (Fick’s law)
  Thermo-hygro-mechanics coupling

## Slide 6: History
  CEASEMT: package of dedicated software:
  COCO (mesh), ESPACE, TEMPS, VISU (post-processing),
  SANSON (eq. properties)
  TEDEL (beams, pipes), TRICO (shells), BILBO (solids)
  PASTEL (2D, plasticity)  INCA
  DELPHINE (thermal), AQUAMODE (modal analysis)
  Start of GIBI (meshing software)
  Initiation of Castem 2000 (based on GIBI)
  Official release of Castem2000
  Procedures, introduction of fluid physics and other physics
  Development of dedicated applications (Toutatis, Esus, …)
  Castem 2000  Cast3M
  Platforms for dev. of dedicated applications (Pléiades, Alliance, …)
  New dedicated applications (Brasero, Gerboise, Rotor, …)
COCO
ESPACE
TEMPS
VISU
SANSON
AQUAMODE
TRICO
TEDEL
DELPHINE
BILBO
INCA
1970
1981
1983
1986
1990
2000

## Slide 7: What, where, how, how much, who?
  Cross platform
      Windows, Linux, macOS
  Where can I download Cast3M?
    http://www-cast3m.cea.fr/index.php?page=dlcastem
  Access to the source code
      Open collaboration
      Compiler / Linker are provided
  Price
      Free license, for education and research use
      Paid license, for enterprise use
  Some users/customers
    Universities, engineering schools …
    IRSN, EDF, SNCF, CNRS, Framatome, Air Liquide, CERN, …
    Reference FEM tool for IRSN for safety analysis of French nuclear installations
    Reference tool for Framatome for fracture mechanics

## Slide 8: How to launch CAST3M?
  1) Write a Gibiane script in a text file
    and save it in a working directory
  2) Open a terminal / command prompt
    and go to the working directory here are some basic Linux commands:
    ls list present files
    cd foo/bar change directory
    pwd print the current working directory
  3) Launch Cast3M on this file
    castem22 hello.dgibi
    You can also use it without .dgibi file
    (interactive mode):
    castem22

## Slide 9: The Cast3M web site
  The Cast3M web site: "the place to be"
  http://www-cast3m.cea.fr
  Cast3M presentation
  Training courses and video tutorials
  Documentation (manual pages, source code, examples)
  Anomaly and development reports
  Downloads
  Contact: Cast3M support
  Community: mailing list, Cast3M club

## Slide 10: Gibiane: The user Langage

## Slide 11: Introduction to GIBIANE
  Language dedicated to FE calculation but also a programming language
    Classical objects (integer, floating-point, string, logical , tables…)
    Flow control statements
    Loops and iterations
    Subroutines
    Recursion
  Interpreted language
    You can run the program as soon as you make changes to the file
    You can run it in a interactive mode
  Object-oriented language
    Everything in the program is treated as an object
    No need to declare variables or to specify the type of a variable
  French key words
  Easy to learn, easy to read

## Slide 12: Gibiane: syntax rules
  Statements lines
    500 characters max per statement
    A statement can be written on several lines
    End with a semicolon ;
    The assignment operator is the equals sign =
  Case insensitive
  TOTO = 3.14 ;
    A = 2. * tOTo ; variable A has the value of 6.28
    excepted characters strings 'blabla' ≠ 'BLABLA' enclosed by single quotes mot1 = 'Hello bro' ;
  Program ends
    with statement FIN ;  Cast3M stop
    empty line or EOF  interactive mode
  A * in the first column means that the rest of the line is a comment
  Empty lines accepted

## Slide 13: Gibiane: syntax rules
  No precedence in operators (from left to rigth)
    1+2*3 = 9  use parentheses
    1+(2*3) = 7
  Prohibitions
    No tab key  incomprehensible error message
    No double quotes "
  Guidelines
    No special characters (é, ç, ~, œ …)
    Use line indentation (with spaces)
    Adjust the text editor
    syntax highlighting, switch tabulations by spaces,…
  Common errors
    Semicolon ; forgotten at the end of the statement
     the statement is not ended
    Single quote ’ forgotten at the end of a string  the string is not ended

## Slide 14: Gibiane: syntax example
  Not good!
    N = 7 ; F = 1 ;i=1;
    REPETER boucle1;
    sI (i <eg N) ;
    f = F * I ;I=i+1;
    SINON;quitter BOUCLE1 ;
    finsi;
    FIN BOUCLE1;
    message F ;FIN ;
  Good!
    ** Initialisation d’un entier N
    N = 7 ;
    ** Calcul de la factorielle du nombre entier N
    F = 1 ;
    I = 1 ;
    REPETER BOUCLE1 ;
    SI (I <EG N) ;
    F = F * I ;
    I = I + 1 ;
    SINON ;
    QUITTER BOUCLE1 ;
    FINSI ;
    FIN BOUCLE1 ;
    ** Affichage du resultat
    MESSAGE F ;
    FIN ;

## Slide 15: Gibiane: objects
  Definition
    Any data/result with a defined type (possibly a sub-type) and name
  Objects Names
    User Defined
    Limited to 8 characters chosen in:
    letters a to z or A to Z, digits (0 to 9) and underscore ( _ )
    Traps
    more than 8 characters: additional characters ignored
    dash sign –  not allowed
    letters with accents: é, è  not allowed
  Objects types
    There are more than 40 types of objects
    A detailed list of the most often used objects is given at the end of the presentation (link)

## Slide 16: Gibiane: objects
  Examples (non exhaustive)
      OBJ1 = 3 ; type: ENTIER (integer)
      OBJ2 = 3.14 ; type: FLOTTANT (floating)
      OBJ3 = 'How are you?' ; type: MOT (string)
      OBJ4 = VRAI ; type: LOGIQUE (logical)
      poin1 = POIN 0. 0. ; type: POINT
      poin2 = POIN 1. 3. ; type: POINT
      OBJ5 = DROI 8 poin1 poin2 ; type: MAILLAGE (mesh)
      LIST OBJ5 ;
      MAILLAGE 3520406 : 8 élément(S) de type SEG2
      0 sous-référence(s)
      1ère ligne numéro élément : 2ème couleur : 3ème... noeud(s)
      1 2 3 4 5 6 7 8
      DEFA DEFA DEFA DEFA DEFA DEFA DEFA DEFA
      1 3 4 5 6 7 8 9
      3 4 5 6 7 8 9 2

## Slide 17: Gibiane: operators
  Definition
    Any processing with a name (Gibiane instruction) that creates new object(s) from pre-existing object(s)
  Operators Names
    Pre-defined
    These are Gibiane instructions
    Case insensitive
    Only the four first characters are necessary and taken into account (DROITE = DROI)
    Excepted abbreviations
    DROI  D (or d)
    CERC  C (or c)

## Slide 18: Gibiane: operators
  Examples of operator call
    Common cases (single object on the left of the equals sign)
    obj1 = OPER obj2 ;
    obj3 = OPER obj4 obj5 ;
    obj6 = obj7 OPER obj8 obj9 ;
    Unusual cases (multiple objects on the left of the equals sign)
    obj1 obj2 obj3 = OPER obj4 obj5 ;
    The "no name" operator: POINTS creation
    in 2 dimensions Point1 = 0. 0. ;
    in 3 dimensions Point1 = 0. 0. 0. ;

## Slide 19: Gibiane: operators
  Arguments order
    do not matters if arguments have different types (with a few exceptions pointed in the manual)
    matters if same type arguments
  Overwriting an object
    Always possible, the overwritten object does not exists any longer
    A = ‘Hello' ;  A has type MOT
    B = 28 ;
    C = 3 ;
    A = B**C ;  A has type ENTIER, its value is 21952
  Traps
    Object name = operator name  operator cannot be called excepted if you call it with quotes A = 'OPER' B C ;
    in upper case!
    Objet name c, C, d or D !

## Slide 20: Gibiane: directives
  Definition
    Statement without assignment operator =
    Does not create a new object
  Examples
    OPTI 'DIME' 3 'ELEM' 'CUB8' ;
    OPTI 'TITR' 'Meshing of the structure' ;
    DEPL mail1 'PLUS' (28. -0.3 20.03) ;
    OPTI is often the first statement of a Gibiane program
    It defines Cast3M general options
    Examples:
      space dimension (1 to 3), elements type, mesh size, output file name, axial symmetry hypothesis, and others…

## Slide 21: Gibiane: procedures
  Definition
    Set of Gibiane statements having a name with input and output arguments
    Similar to Fortran subroutine or a C function
  Procedures names
    As other objects (a procedure is an object with PROCEDUR type)
  Declaration
    DEBP my_proc arg_e1*entier arg_e2*flottant ... arg_en*mchaml ;
    statement 1 ;
    statement 2 ;
    ...
    statement k ;
    FINP arg_s1 arg_s2 ... arg_sm ;

## Slide 22: Gibiane: procedures
  Calling
    As an operator or directive
    obj1 obj2 ... objm = my_proc ent1 flot2 ... champn ;
  Pre-existing procedures in Cast3M
    List in: http://www-cast3m.cea.fr/index.php?page=notices
    PASAPAS  non-linear calculations
    FLAMBAGE  buckling calculations
    DYNAMIC  dynamics calculations
    THERMIC  thermal calculations
    G_THETA  line integrals computation (fracture)
    …
    other procedures to discover in the manual pages

## Slide 23: Gibiane: procedures
  Traps
    FINP missing
     Cast3M stops, error message that can be misunderstood
    FINP existing but missing ;
     Cast3M stops, error message that can be misunderstood
    Procedure called before it is declared
     Cast3M stops, error message in the = operator difficult to interpret

## Slide 24: Gibiane: some useful statements
  Debugging
    INFO OPER ; OPTI 'LANG' 'ANGL' ;
     print the manual page of a operator/directive/procedure
    OPTI 'DONN' 5 ;
     stop to run the file .dgibi
     run from scream: interactive prompt
    OPTI 'DONN' 3 ;
     return to run the file .dgibi (from where it stops previously)
    LIST OBJ1 ;
     print information about the object OBJ1
    LIST 'RESU' OBJ1 ;
     printing is reduced to the headings
    OPTI 'DEBU' 1 ;
     stop on a error inside a procedure
    TRAC OBJ1 (OBJ2) ;
     plot an object (mesh, iso-values of fields, deformed mesh, …)
    MESS 'Here I am!' ;
     print a message

## Slide 25: Documentation
  Manual pages of operators/directives/procedures
    1) The INFO directive, example: INFO EXTR ;
    2) Local html page: in the installation directory
    example on a Linux system: /home/john_doe/CAST3M_2022/doc/index.html
    example on a Windows system: C:\Cast3M\PCW_22\doc\index.html
    3) The web site: http://www-cast3m.cea.fr/index.php?page=notices
    dedicated to the up to date version !
  Users manual
    On the web site, see the "Documentation" tab

## Slide 26: Tutorial classes Modeling of the Thermo-mechanical behavior of A structure with a circular cavity

## Slide 27: Problem Description and boundary conditions
Convection
Prescribed temperature
Surface force
Blocking (symetry)
Thermal
Mechanical
Surface heat flux
Radiation
Volume heat source
Volume force (weight)

## Slide 28: reminder
  Method to perform finite element calculations (4 main steps)
    1) Geometry description and meshing
      a) Description of points, lines, surfaces, volumes
      b) Discretization
    2) Mathematical model definition
      a) Definition of the model data (type of analyze, formulation, material behavior, types of elements)
      b) Definition of the material properties (Young’s modulus, density, …)
      c) Definition of the geometrical properties (shell thickness, moments of inertia for beams, …)
      d) Definition of the boundary conditions and loadings
      f) Definition of the initial values
    3) Solving the discretized model
      a) Elementary stiffness matrix and elementary mass matrix calculation
      b) Global matrix calculation
      c) Introduction of the loadings and boundary conditions
      e) Solving the system of equations
    4) Analysis et post-processing
      a) Local quantities (strains, stresses, displacements, …)
      b) Global quantities (maximal strains, strain energy, …)

## Slide 29: solution files
  The solution files of this tutorial are in the examples base
    Download them from the web site:
    http://www-cast3m.cea.fr/index.php?page=exemples
    Three files will be used:
  formation_debutant_1_maillage.dgibi
  formation_debutant_2_thermique.dgibi
  formation_debutant_3_mecanique.dgibi

## Slide 30: Chap. 1: Geometry and mesh
  Objective: to create a parametered mesh of the plate with the hole
  locate the main points
  mesh the closed border
  mesh the internal surface
X
Y
O
haut
long
rayon
nlong
nhaut
nbasg
nbasd
nqcg
nqcd

## Slide 31: Chap. 1: Meshing and general statements
  General options and parameters
  * GENERAL OPTIONS AND TYPE OF FINITE ELEMENTS
  OPTI 'DIME' 2 'ELEM' 'QUA8' ;
  * LENGTHS AND MESH DENSITY DEFINITIONS
  LONG = 24.E-1 ;
  HAUT = 10.E-1 ;
  RAYON = 2.E-1 ;
  NLONG = 24 ;
  NHAUT = 4 ;
  NBASG = 10 ;
  NBASD = 10 ;
  NQCG = 8 ;
  NQCD = 8 ;
New objects ENTIER, FLOTTANT, MOT
X
Y
O
haut
long
rayon
nlong
nhaut
nbasg
nbasd
nqcg
nqcd

## Slide 32: Chap. 1: Meshing and general statements
  Points creation
  * CREATION OF POINTS SUPPORTING THE MESH
  PA = 0. 0. ;
  PB = ((0.5 * LONG) – RAYON) 0. ;
  PC = (0.5 * LONG) RAYON ;
  PD = ((0.5 * LONG) + RAYON) 0. ;
  PE = LONG 0. ;
  PF = LONG HAUT ;
  PG = 0. HAUT ;
  PCEN = (0.5 * LONG) 0. ;
new object POINT
PA
PB
PC
PD
PE
PF
PG
PCEN

## Slide 33: Chap. 1: Meshing and general statements
  Lines and closed contour
  * STRAIGHT LINES CONSTRUCTION (DROI or D)
  LIAB = DROI NBASG PA PB ;
  LIDE = DROI NBASD PD PE ;
  LIEF = D NHAUT PE PF ;
  LIFG = D NLONG PF PG ;
  LIGA = D NHAUT PG PA ;
  * CONSTRUCTION OF CIRCLES (CERC or C)
  (It’s up to you: see the manual pages)
  * CLOSED CONTOUR OBTAINED FROM THE ELEMENTARY LINES ASSEMBLY
  CO = LIAB ET CE ET LIDE ET LIEF ET LIFG ET LIGA ;
new object MAILLAGE

## Slide 34: Chap. 1: Meshing and general statements
  Lines and closed contour
  * STRAIGHT LINES CONSTRUCTION (DROI or D)
  LIAB = DROI NBASG PA PB ;
  LIDE = DROI NBASD PD PE ;
  LIEF = D NHAUT PE PF ;
  LIFG = D NLONG PF PG ;
  LIGA = D NHAUT PG PA ;
  * CONSTRUCTION OF CIRCLES (CERC or C)
  CE1 = CERC NQCG PB PCEN PC ;
  CE = C NQCD CE1 PCEN PD ;
  * CLOSED CONTOUR OBTAINED FROM THE ELEMENTARY LINES ASSEMBLY
  CO = LIAB ET CE ET LIDE ET LIEF ET LIFG ET LIGA ;
LIAB
CE
LIFG
LIDE
LIEF
LIGA

## Slide 35: Chap. 1: Meshing and general statements
  Surface meshing (free meshing inside the closed contour)
  SU = SURF CO ;
  TRAC SU ;

## Slide 36: Chap. 1: Meshing and general statements
  Objective: to create a regular mesh of the half-plate with a hole
- contains only quadrangle
- controlled elements size
- respect the symmetry of the shape

## Slide 37: Chap. 1: Meshing and general statements
  Objective: to create a regular mesh of the half-plate with a hole
  regular mesh, symmetry, variable elements size
variable density 0.1 – 0.05
PA
PB
PC
PD
PE
PF
PG
PCEN
PH
nhaut = 10
nqcg = 20

## Slide 38: Chap. 1: Meshing and general statements
  Surface meshing (regular mesh surface relative to two lines)
  NHAUT = 10 ;
  NQCG = 20 ;
  PH = (locate point PH  POIN)
  LIHG = (define line HG  DROI)
  LIGA = (define line GA  DROI)
  CE1 = (define quarter-circle CE1  CERC)
  SU1 = (mesh the surface SU1  REGL)
  SU2 = (using symmetry mesh the surface SU2  SYME)
  SU = (group the two meshes SU1 and SU2  ET)

## Slide 39: Chap. 1: Meshing and general statements
  Surface meshing (regular mesh surface relative to two lines)
  NHAUT = 10 ;
  NQCG = 20 ;
  PH = (0.5 * LONG) HAUT ;
  LIHG = DROI (NQCG - NHAUT) PH PG ;
  LIGA = DROI NHAUT PG PA ;
  CE1 = CERC NQCG PB PCEN PC ;
  SU1 = REGL 'DINI' 0.05 'DFIN' 0.1 (INVE CE1) (LIHG ET LIGA) ;
  SU2 = SU1 SYME 'DROI' PCEN PH ;
  SU = SU1 ET SU2 ;
  TRAC SU ;

## Slide 40: Chap. 1: Meshing and general statements
  Elimination of double nodes, directive ELIM
  ELIM SU 1.E-9 ;
  TRAC SU ;
     all SU nodes distant less than 10-9 m are merged in a single one
     does not change the element type
     directive to use carefully !
  See also REGE operator
     regeneration of elements with merged nodes
     change the element type if necessary

## Slide 41: Chap. 1: Meshing and general statements
  Meshed zones recovery
  * HALF-CIRCLE MESH, UPPER AND LINES MESHES RETRIEVAL WITH 'POIN' ET 'ELEM'
  CSU = CONT SU ; (Contour of SU mesh recovery)
  PCE = SU POIN 'SPHE' PCEN PC 1.E-9 ; (Points of SU located on sphere recovery)
  CE = CSU ELEM 'APPU' 'STRI' PCE ; (Elements containing points of CE recovery)
  PLHAUT = (It’s up to you); (Points of line PF PG recovery)
  LHAUT = (It’s up to you); (Elements containing points of PLHAUT recovery)
  PLBAS = (It’s up to you); (Points of line PA PE recovery)
  LBAS = (It’s up to you); (Elements containing points of PLBAS recovery)

## Slide 42: Chap. 1: Meshing and general statements
  Meshed zones recovery
  * HALF-CIRCLE MESH, UPPER AND LINES MESHES RETRIEVAL WITH 'POIN' ET 'ELEM'
  CSU = CONT SU ;
  PCE = SU POIN 'SPHE' PCEN PC 1.E-9 ;
  CE = CSU ELEM 'APPU' 'STRI' PCE ;
  PLHAUT = SU POIN 'DROI' PF PG 1.E-9 ;
  LHAUT = CSU ELEM 'APPU' 'STRI' PLHAUT ;
  PLBAS = SU POIN 'DROI' PE PCEN 1.E-9 ;
  LBAS = CSU ELEM 'APPU' 'STRI' PLBAS ;

## Slide 43: [Bonus] 3D Meshing
  Volume meshing (complement)
  * CHANGE TO DIMENSION 3
  OPTI 'DIME' 3 'ELEM' 'CU20' ;
  * VOLUME FROM EXTRUSION
  VO = SU VOLU 6 'TRAN' (0. 0. 2.) ;
  * VOLUME FROM ROTATION
  VO = SU VOLU 10 'ROTA' 90. (0. -1. 0.) (1. -1. 0.) ;
  * DISPLAYING
  TRAC VO ;
  TRAC 'CACH' VO ;
  OPTI 'TRAC' 'OPEN' ;
  TRAC 'CACH' VO ;
  * BACK TO DIMENSON 2
  OPTI 'DIME' 2 ;

## Slide 44: Chap. 1: Meshing and general statements
  Saving data and end of program
  * NAME OF THE OUTPUT FILE
  OPTI 'SAUV' 'formation_debutant_1_maillage.sauv' ;
  * WRITTING THE FILE
  SAUV ;
  * END OF THE GIBI PROGRAM
  FIN ;
  All of the objects are saved in the output file
  The output file is binary (XDR format )
  Other formats available (text, …), see the manual page of OPTI 'SAUV' and SAUV

## Slide 45: Thermal analysis: reminder
  Heat equation
    on
    with:
    : temperature
    : volume heat flux source
    : thermal conductivity
    : volumetric mass density
    : specific heat capacity
    : time
  Boundary conditions
    Prescribed temperatures on
    Prescribed surface heat flux
    on

## Slide 46: Thermal analysis: reminder
  Discrete form (finite elements)
    FE discretization:
    Weak formulation + EF:
    Matrices
    capacity matrix (J.K-1)
    conductivity matrix (W.K-1)
    Equivalent nodal flux vectors (W)

## Slide 47: Chap. 2: stationary linear thermal Analysis
  Objective: stationary thermal calculation with prescribed temperatures (time independent)
   Linear system
  conductivity matrix calculation (1st member)
  fixed nodal heat fluxes calculation (2nd member)
  solving with RESO  temperature (unknown)
250 °C
-3,5 104 W.m-2

## Slide 48: Chap. 2: stationary linear thermal Analysis
  Input data from previous computation (mesh, parameters, …)
  * NAME OF THE INPUT FILE (RESTITUTION)
  OPTI 'REST' 'formation_debutant_1_maillage.sauv' ;
  * LOADING INTO MEMORY
  REST ;
   All of the objects are loaded into memory
   They can be called now
  * MATERIAL PROPERTIES
  CONDUMAT = 210. ;
  CAPAMAT = 900. ;
  RHOMAT = 2700. ;
  * INITIAL AND REFERENCE TEMPERATURE
  T0 = 25. ;

## Slide 49: Chap. 2: stationary linear thermal Analysis
  Mathematical formulation
  * THERMAL MODEL (CONDUCTION) UNIFORM AND STATIONARY MATERIAL PROPERTIES
  MOT = MODE SU 'THERMIQUE' ;
  MAT = MATE MOT 'K' CONDUMAT 'C' CAPAMAT 'RHO' RHOMAT 'TINI' T0 ;
  * CONDUCTIVITY MATRIX CALCULATION (FIRST MEMBER)
  CON = COND MOT MAT ;
new objects MMODEL, MCHAML, RIGIDITE

## Slide 50: Chap. 2: stationary linear thermal Analysis
  Boundary conditions
  * BOUNDARY CONDITIONS: PRESCRIBED TEMPERATURE ON THE HOLE
  BLT = BLOQ CE 'T' ;
  * NODAL HEAT FLUX (LOADINGS) FOR CONSTRAINTS link
  TMAX = 250. ;
  FLT1 = DEPI BLT TMAX ;
  * PRESCRIBED HEAT FLUX ON THE LEFT SIDE
  FLT2 = FLUX MOT LIGA -3.5E4 ;
  Linear system solving
  * TEMPERATURE FIELD CALCULATION USING 'RESO'
  TCON1 = RESO (CON ET BLT) (FLT1 ET FLT2) ;
new object CHPOINT

## Slide 51: Chap. 2: stationary linear thermal Analysis
  Results display
  * DISPLAY THE TEMPERATURE FIELD
  TRAC TCON1 SU ;

## Slide 52: Chap. 2: stationary linear thermal Analysis
  Results display
  * DISPLAY THE TEMPERATURE FIELD
  TRAC TCON1 SU CSU ;

## Slide 53: Chap. 2: stationary linear thermal Analysis
  Results display
  * DISPLAY THE TEMPERATURE FIELD
  LISO1 = PROG 0. 'PAS' (TMAX / 15.) TMAX ;
  TRAC TCON1 SU CSU LISO1 ;
new object LISTREEL

## Slide 54: Chap. 2: stationary linear thermal Analysis
  Results display
  * DISPLAY THE TEMPERATURE FIELD
  TRAC TCON1 SU CSU LISO1 'TITR' '[2] Temperature' ;

## Slide 55: Chap. 2.1: stationary linear thermal Analysis convection and volume heat source
  Objective: previous thermal calculation
    + convection
    + volume heat source
  convection model
  volume source load
-3,5 104 W.m-2
250 °C
T∞ = 25 °C h = 100 W.K-1.m-2
105 W.m-3

## Slide 56: Chap. 2.1: stationary linear thermal Analysis convection and volume heat source
  Mathematical formulation
  * CONVECTION MODEL
  MOC = MODE LHAUT 'THERMIQUE' 'CONVECTION' ;
  MAC = MATE MOC 'H' 100. ;
  Conductivity matrix (but for convection !)
  * FIRST MEMBER FOR CONVECTION
  CONH = COND MOC MAC ;
  Equivalent nodal heat flux vector (convection)
  * SECOND MEMBER FOR CONVECTION
  CHTC = MANU 'CHPO' LHAUT 'T' T0 ;
  FLH = CONV MOC MAC CHTC ;

## Slide 57: Chap. 2.1: stationary linear thermal Analysis convection and volume heat source
  Equivalent nodal heat flux vector (volume source)
  * SECOND MEMBER FOR THE VOLUME SOURCE
  X Y = COOR SU ;
  PT1 = X POIN 'SUPERIEUR' 20.E-1 ;
  PT2 = (REDU Y PT1) POIN 'INFERIEUR' 5.E-1 ;
  ELSOU = SU ELEM 'APPUYE' 'STRICTEMENT' PT2 ;
  FLS = SOUR (REDU MOT ELSOU) 1.E5 ELSOU ;
  Linear system solving
  * TEMPERATURE FIELD CALCULATION USING 'RESO'
  TCON2 = RESO (CON ET CONH ET BLT) (FLT1 ET FLT2 ET FLH ET FLS) ;
  * DISPLAY THE TEMPERATURE FIELD
  TRAC TCON2 SU CSU LISO1 ;

## Slide 58: Note: the nodal field (CHPOINT)
  The CHPOINT type object
  Values are located on POINTS (nodes)
  Examples:
  scalar temperature field
  vector displacement field (3 components)
  vector coordinates fields
  second member of a linear problem , for instance:
      nodal forces
      nodal heat flux
  and others…
  Some characteristics:
  only one value per node
  do not depends on the mesh, only on nodes!
  when plotted, the field is continuous on the mesh

## Slide 59: Note: the element field (MCHAML)
  The MCHAML type object
  Values are located into ELEMENTS of a mesh
  Examples:
  material properties
  stress, strains fields
  internal variables field
  gradient of a CHPOINT object
  and others…
  Some characteristics:
  several support points available:
      integration points for stresses
      integration points for stiffness
      integration points for mass
      center of gravity
      nodes
  interpolation functions depends on the model
  non continuous between elements

## Slide 60: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Objective: previous thermal calculation
  + transient (with an initial temperature = 25 °C)
  time description of loading
  initial conditions
  using the PASAPAS solving procedure
T∞ = 25 °C h = 100 W.K-1.m-2
105 W.m-3
-3,5 104 W.m-2
250 °C

## Slide 61: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
new objects EVOLUTIOn and CHARGEMEnt
  Initial conditions
  * FINAL INSTANT
  TPSFIN = 5.E4 ;
  Loading definition (BC as function of space and time)
  * TEMPERATURE LOAD
  LIST1 = PROG 0. (0.1 * TPSFIN) TPSFIN ;
  LIST2 = PROG (T0 / TMAX) 1. 1. ;
  EVT1 = EVOL 'MANU' LIST1 LIST2 ;
  CHATIMP = CHAR 'TIMP' FLT1 EVT1 ;
  * HEAT FLUX LOAD
  LIST3 = PROG 0. (0.2 * TPSFIN) (0.4 * TPSFIN) TPSFIN ;
  LIST4 = PROG 0. 0. 1. 1. ;
  EVT2 = EVOL 'MANU' LIST3 LIST4 ;
  CHAFIMP = CHAR 'Q' FLT2 EVT2 ;
  * CONVECTION TEMPERATURE LOAD
  LIST5 = PROG 0. TPSFIN ;
  LIST6 = PROG 1. 1. ;
  EVCTE = EVOL 'MANU' LIST5 LIST6 ;
  CHACONV = CHAR 'TECO' CHTC EVCTE ;
  * HEAT SOURCE LOAD
  CHASOUR = CHAR 'Q' FLS EVT2 ;
  CHAT = CHATIMP ET CHAFIMP ET CHACONV ET CHASOUR ;
t / TPSFIN
0
k
1
EVT1
0,1
0,2
1
0,1
0,4
EVCTE
EVT2
Loading

## Slide 62: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Construction of TAB1: table for procedure PASAPAS
  * TABLE OF ARGUMENTS NECESSARY AS ENTRIES FOR THE PASAPAS PROCEDURE
  TAB1 = TABL ;
  TAB1 . 'MODELE' = MOT ET MOC ;
  TAB1 . 'CARACTERISTIQUES' = MAT ET MAC ;
  TAB1 . 'BLOCAGES_THERMIQUES' = BLT ;
  TAB1 . 'CHARGEMENT' = CHT ;
  TAB1 . 'TEMPS_CALCULES' = PROG 0. 'PAS' (0.02 * TPSFIN) TPSFIN ;
  Solving with PASAPAS procedure
  * PASAPAS CALL
  PASAPAS TAB1 ;
new object TABLE

## Slide 63: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Post processing: evolution curves, field plot
  * VARIATION OF TEMPERATURE AT TWO POINTS AS A FUNCTION OF TIME
  * IN ORDER TO VERIFY STEADY STATE IS REACHED
  PMIL = SU POIN 'PROC' ((0.5 * LONG) (0.5 * HAUT)) ;
  EV1 = EVOL 'ROUG' 'TEMP' TAB1 'TEMPERATURES' 'T' PMIL ;
  EV2 = EVOL 'BLEU' 'TEMP' TAB1 'TEMPERATURES' 'T' PG ;
  DESS (EV1 ET EV2) ;

## Slide 64: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Post processing: iterative loop for plotting
  * LOOP ON EACH TIME STEP AND PLOT OF TEMPERATURE FIELD
  N1 = DIME (TAB1 . 'TEMPERATURES') ;
  REPE B1 N1 ;
  T_I = TAB1 . 'TEMPERATURES' . (&B1 - 1) ;
  TPS_I = TAB1 . 'TEMPS' . (&B1 - 1) ;
  PRC_I = ENTI (100. * TPS_I / TPSFIN) ;
  MOT_I = CHAI '[3] Temperatures at time ' TPS_I ' (' PRC_I ' %)' ;
  TRAC T_I SU CSU 'TITR' MOT_I LISO1 ;
  FIN B1 ;
Loop counter
1, 2, 3, … , N1

## Slide 65: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Procedure writing (heat flux vector calculation)
  * HEAT FLUX VECTOR ==> PROCEDURE WRITING
  DEBP VECFLU CHP1*'CHPOINT' MOD1*'MMODEL' MAT1*'MCHAML' ;
  * GRADIENT CALCULATION AND CHANGE OF ITS TYPE
  G1 = GRAD CHP1 MOD1 ;
  G2 = CHAN 'TYPE' G1 'CARACTERISTIQUES' ;
  * MULTIPLICATION OF THE ELEMENT FIELDS
  Q = MAT1 * G2 (MOTS 'K' 'K') (MOTS 'T,X' 'T,Y') (MOTS 'QX' 'QY') ;
  Q = -1. * Q ;
  * VECTOR OBJECT CREATION
  VEC1 = VECT Q MOD1 (MOTS 'QX' 'QY') 2.E-6 ;
  FINP VEC1 ;
new objects PROCEDURe, LISTMOTS, VECTEUR

## Slide 66: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Post processing: heat flux vector plot
  * LOOP ON EACH TIME STEP AND PLOT OF HEAT FLUX VECTOR
  REPE B1 N1 ;
  T_I = TAB1 . 'TEMPERATURES' . (&B1 - 1) ;
  VF_I = VECFLU T_I MOT MAT ;
  TRAC VF_I CSU ;
  FIN B1 ;

## Slide 67: Chap. 3: Transient linear thermal analysis convection, source, pASAPAS
  Post processing: plot of heat flux vector and temperature isovalue lines
  * FLUX VECTOR AND TEMPERATURE FIELD AS ISOVALUE LINES
  OPTI 'ISOV' 'LIGN' ;
  TRAC VF_I T_I SU CSU 15 ;
  OPTI 'ISOV' 'SURF' ;

## Slide 68: Chap. 4: Transient NON-linear thermal analysis convection, source, RADIATION, PASAPAS
  Objective: previous thermal calculations
  + radiation
  addition of a model and loading for radiation
-3,5 104 W.m-2
250 °C
T∞ = 25 °C h = 100 W.K-1.m-2
105 W.m-3
T∞ = 25 °C ε = 0.8

## Slide 69: Chap. 4: Transient NON-linear thermal analysis convection, source, RADIATION, PASAPAS
  Radiation heat transfer model
  * RADIATION MODEL ON THE UPPER LINE
  MOR = MODE LHAUT 'THERMIQUE' 'RAYONNEMENT' 'INFINI' ;
  MAR = MATE MOR 'EMIS' 0.8 ;
  Loading with the surroundings temperature
  * RADIATION LOADING IS THE SURROUNDINGS TEMPERATURE
  CHTR = MANU 'CHPO' LHAUT 1 'T' T0 ;
  CHARAYE = CHAR 'TERA' CHTR EVCTE ;
  CHAT = CHAT ET CHARAY ;

## Slide 70: Chap. 4: Transient NON-linear thermal analysis convection, source, RADIATION, PASAPAS
  PASAPAS table building
  * RE-DEFINITION OF TABLE TAB1 FOR PASAPAS PROCEDURE
  TAB1 = TABL ;
  TAB1 . 'MODELE' = (It’s up to you) ;
  TAB1 . 'CARACTERISTIQUES' = (It’s up to you) ;
  TAB1 . 'BLOCAGES_THERMIQUES' = (It’s up to you) ;
  TAB1 . 'CHARGEMENT' = (It’s up to you) ;
  TAB1 . 'TEMPS_CALCULES' = (It’s up to you) ;
  Other indexes ?? (It’s up to you)
  Solving with PASAPAS procedure
  * PASAPAS CALL
  (It’s up to you)

## Slide 71: Chap. 4: Transient NON-linear thermal analysis convection, source, RADIATION, PASAPAS
  Post processing
  * RE-DEFINITION OF TABLE TAB1 FOR PASAPAS PROCEDURE
  TAB1 = TABL ;
  TAB1 . 'MODELE' = MOT ET MOC ET MOR ;
  TAB1 . 'CARACTERISTIQUES' = MAT ET MAC ET MAR ;
  TAB1 . 'BLOCAGES_THERMIQUES' = BLT ;
  TAB1 . 'CHARGEMENT' = CHAT ;
  TAB1 . 'TEMPS_CALCULES' = PROG 0. 'PAS' (0.02 * TPSFIN) TPSFIN ;
  TAB1 . 'CELSIUS' = VRAI ;
  Solving with PASAPAS procedure
  * PASAPAS CALL
  PASAPAS TAB1 ;

## Slide 72: Chap. 4: Transient NON-linear thermal analysis convection, source, RADIATION, PASAPAS
  Post processing
  * TIME EVOLUTION OF TEMPERATURE ON 2 POINTS
  EV11 = EVOL 'ROUG' 'TEMP' TAB1 'TEMPERATURES' 'T' PMIL ;
  EV22 = EVOL 'BLEU' 'TEMP' TAB1 'TEMPERATURES' 'T' PG ;
  TL = TABL ;
  TL . 1 = 'TIRR' ;
  TL . 2 = 'TIRR' ;
  TL . 'TITRE' = TABL ;
  TL . 'TITRE' . 1 = 'PMIL' ;
  TL . 'TITRE' . 2 = 'PG ' ;
  TL . 'TITRE' . 3 = 'PMIL with rad' ;
  TL . 'TITRE' . 4 = 'PG with rad' ;
  DESS (EV1 ET EV2 ET EV11 ET EV22) 'LEGE' TL ;

## Slide 73: Chap. 4: Transient NON-linear thermal analysis convection, source, RADIATION, PASAPAS
  Saving data and end of program
  OPTI 'SAUV' 'formation_debutant_2_thermique.sauv' ;
  SAUV ;
  FIN ;

## Slide 74: Mechanics: reminder
  Equilibrium equation (statics)
    on
  Boundary conditions
    Prescribed displacements: on
    Prescribed surface forces: on
    with:
    : displacement vector
    : stress tensor
    : volume forces vector
    : normal vector to a surface

## Slide 75: Mechanics: reminder
  FE discretization
  Weak formulation of equilibrium + FE discretization
    Equivalent nodal forces vector (N) to:
    prescribed surface forces
    surface forces in reaction to prescribed displacements
    prescribed volume forces
    internal volume forces
    Matrices
    matrix of shape functions ( . )
    matrix of derivative of shape functions (m-1)

## Slide 76: Mechanics: reminder
  FE discretization
  Weak formulation of equilibrium + FE discretization
  Small strain hypothesis + elasticity
    Matrices
    stiffness matrix (N. m-1)

## Slide 77: Chap. 5: elastic mechanical analysis
  Objective: elastic calculations
  with prescribed displacements
  and surface and volume forces
   Linear system
  stiffness matrix calculation (1st member)
  nodal forces calculation (2nd member)
  solving with RESO  displacements (unknown)
σ = 30 MPa
Ux = 0
Uy = 0
f = ρg

## Slide 78: Chap. 5: elastic mechanical analysis
  Input data from previous computation (mesh, parameters, …)
  OPTI 'REST' 'formation_debutant_2_thermique.sauv' ;
  REST ;
    * MECHANICAL MATERIAL PARAMETERS
  YOUNGMAT = 30.E9 ;
  NUMAT = 0.2 ;
  ALPHAMAT = 12.E-6 ;
  SIGYMAT = 120.E6 ;
  Plane strain hypothesis
  OPTI 'MODE' 'PLAN' 'DEFO' ;
  Linear elastic isotropic mechanical model
  MOM1 = MODE SU 'MECANIQUE' 'ELASTIQUE' ;
  MAM1 = MATE MOM1 'YOUN' YOUNGMAT 'NU' NUMAT 'ALPH' ALPHAMAT 'TREF' T0 'TALP' T0 ;

## Slide 79: Chap. 5: elastic mechanical analysis
  Stiffness matrix (1st member)
  RI = RIGI MOM1 MAM1 ;
  Constraints on displacements (1st member)
  BLMX = BLOQ PA 'UX' ; (point A locked along x)
  BLMY = BLOQ (It's up to you); (lower line locked along y)
  RITOT = (It's up to you); (assembly of stiffness)
  Equivalent nodal forces to the pressure (2nd member)
  FS = PRES (It's up to you);
  Equivalent nodal forces to the volume forces (2nd member)
  FV = CNEQ (It’s up to you);
  Linear system solving
  U5 = (It's up to you)

## Slide 80: Chap. 5: elastic mechanical analysis
  Stiffness matrix (1st member)
  RI = RIGI MOM1 MAM1 ;
  Constraints on displacements (1st member)
  BLMX = BLOQ PA 'UX' ; (point A locked along x)
  BLMY = BLOQ LBAS 'UY' ;
  RITOT = RI ET BLMX ET BLMY ;
  Equivalent nodal forces to the pressure (2nd member)
  FS = PRES 'MASS' MOM1 LHAUT 30.E6 ;
  Equivalent nodal forces to the volume forces (2nd member)
  ROG = MANU 'CHPO' SU 2 'FX' 0. 'FY' (-9.81 * RHOMAT) ;
  FV = CNEQ MOM1 ROG ;
  Linear system solving
  U5 = RESO RITOT (FS ET FV) ;

## Slide 81: Chap. 5: elastic mechanical analysis
  Post processing: strains, stresses, deformed mesh
  * DEFORMED MESH PLOT
  DEF_5 = DEFO SU U5 150. 'ROUG' ;
  DEF_INI = DEFO SU U5 0. ;
  TRAC (DEF_INI ET DEF_5) ;
  * PLOT OF THE DEFORMED MESH BORDER
  (It's up to you)
new object DEFORMEE

## Slide 82: Chap. 5: elastic mechanical analysis
  Post processing: strains, stresses, deformed mesh
  * DEFORMED MESH PLOT
  DEF_5 = DEFO SU U5 150. 'ROUG' ;
  DEF_INI = DEFO SU U5 0. ;
  TRAC (DEF_INI ET DEF_5) ;
  * PLOT OF THE DEFORMED MESH BORDER
  DEF_5C = DEFO CSU U5 150. 'ROUG' ;
  DEF_INIC = DEFO CSU U5 0. ;
  TRAC (DEF_INIC ET DEF_5C) ;
new object DEFORMEE

## Slide 83: Chap. 5: elastic mechanical analysis
  Post processing: strains, stresses, deformed mesh
  With two statements:
  * STRAINS CALCULATION
  DEF = EPSI U5 MOM1 'LINE' ;
  * STRESSES CALCULATION FROM STRAINS
  SIG = ELAS DEF MOM1 MAM1 ;
  With one statement:
  * STRESSES CALCULATION FROM DISPLACEMENTS
  SIG = SIGM U5 MOM1 MAM1 'LINE' ;

## Slide 84: Chap. 5: elastic mechanical analysis
  Post processing: stresses on the deformed mesh
  * STRESSES PLOT ON THE INITIAL SHAPE
  TRAC (It's up to you) ;

## Slide 85: Chap. 5: elastic mechanical analysis
  Post processing: stresses on the deformed mesh
  * STRESSES PLOT ON THE INITIAL SHAPE
  TRAC SIG MOM1 ;
  * STRESSES PLOT ON THE DEFORMED SHAPE
  DEF_5B = DEFO SU U5 150. ;
  TRAC SIG MOM1 DEF_5B CSU ;

## Slide 86: Chap. 5: elastic mechanical analysis
  Post processing: stresses at Gauss points
  * STRESS PLOT ON THE MESH
  SIGYY = EXCO SIG 'SMYY' ;
  MESS 'Mini and Maxi for Sigma YY : ' (MINI SIGYY) (MAXI SIGYY) ;
  TRAC SIGYY MOM1 ;
  SIGYYG = CHAN 'CHPO' SIGYY MOM1 'SUPP' ;
  MPGAUSS = EXTR SIGYYG 'MAIL' ;
  TRAC SIGYYG MPGAUSS ;

## Slide 87: Chap. 5: elastic mechanical analysis
  Post processing: stress concentration evolution curve (along the lower side)
  SIGB = CHAN 'CHPO' SIG MOM1 ;
  LBASG = LBAS ELEM 'COMP' PB PA ;
  EVSIG = EVOL 'CHPO' SIGB 'SMYY' LBASG ;
  EVK = (ABS EVSIG) / 30.E6 ;
  DESS EVK ;

## Slide 88: Chap. 5: elastic mechanical analysis
  Post processing: evolution along any line
  OPTI 'ELEM' 'SEG2' ;
  LIG1 = DROI 50 (0.1 0.1) (2.3 0.9) COUL 'ORAN' ;
  TRAC (CSU ET LIG1) ;
  SIGT = CHAN 'NOEUD' MOM1 SIG ;
  SIGLBAS = PROI SIGT LIG1 ;
  EVSIG2 = EVOL 'ORAN' 'CHPO' SIGLBAS 'SMXY' LIG1 ;
  DESS EVSIG2 ;

## Slide 89: Chap. 5: elastic mechanical analysis
  Post processing: force reaction
  * SUPPORTS REACTIONS PLOT AS VECTORS
  REAC1 = REAC U5 (BLMX ET BLMY) ; (reaction due to a constraint)
  VREAC = VECT REAC1 'FORC' 'ROUG' ; (arrows for plotting)
  * IDEM FOR APPLIED FORCES
  VFIMP = (It's up to you)
  TRAC (It's up to you) ;

## Slide 90: Chap. 5: elastic mechanical analysis
  Post processing: force reaction
  * SUPPORTS REACTIONS PLOT AS VECTORS
  REAC1 = REAC U5 (BLMX ET BLMY) ; (reaction due to a constraint)
  VREAC = VECT REAC1 'FORC' 'ROUG' ; (arrows for plotting)
  * IDEM FOR APPLIED FORCES
  VFIMP = VECT FS 'FORC' 'VERT' ;
  TRAC (VFIMP ET VREAC) CSU ;

## Slide 91: Chap. 5: elastic mechanical analysis
  Bonus: case with prescribed displacements
  * STIFFNESS MATRICES (1ST MEMBER) link
  BLMY2 = BLOQ LHAUT 'UY' ;
  RITOT2 = RI ET BLMX ET BLMY ET BLMY2 ;
  * SECOND MEMBER ASSOCIETED TO THE STIFFNESS MATRIX
  FU = DEPI BLMY2 (8.E-3 * RAYON) ;
  * RESOLUTION
  U52 = RESO RITOT2 (FU ET FV) ;
  * POST PROCESSING
  DEF_5C2 = DEFO CSU U52 150. 'VERT' ;
  TRAC (DEF_INIC ET DEF_5C ET DEF_5C2) ;

## Slide 92: Chap. 6: Linear elasticity THERMAL LOADING
  Objective: previous mechanical calculation
  + thermal loading
  thermal strain calculation
  add the nodal forces equivalent to the thermal strain (link)
+

## Slide 93: Chap. 6: Linear elasticity THERMAL LOADING
  Nodal forces resulting from thermal strain (2nd member)
  * THERMAL STRAINS FROM TEMPERATURE FIELD CALCULATED
  * TAKING INTO ACCOUNT CONVECTION + RADIATION
  TFINAL = TAB1 . 'TEMPERATURES' . (N1 - 1) ;
  EPT = EPTH TFINAL MOM1 MAM1 ;
  * PSEUDO STRESS FROM THERMAL STRAINS
  SIT = ELAS EPT MOM1 MAM1 ;
  * NODAL FORCES FROM THIS STRESS
  FT = BSIG SIT MOM1 ;
  Linear system solving (additional term to the 2nd member)
  * DISPLACEMENTS CALCULATION BY CALLING SOLVER WITH THERMAL PSEUDO FORCES
  * ADDED TO THE MECHANICAL ONES
  U6 = (It's up to you);

## Slide 94: Chap. 6: Linear elasticity THERMAL LOADING
  Nodal forces resulting from thermal strain (2nd member)
  * THERMAL STRAINS FROM TEMPERATURE FIELD CALCULATED
  * TAKING INTO ACCOUNT CONVECTION + RADIATION
  TFINAL = TAB1 . 'TEMPERATURES' . (N1 - 1) ;
  EPT = EPTH TFINAL MOM1 MAM1 ;
  * PSEUDO STRESS FROM THERMAL STRAINS
  SIT = ELAS EPT MOM1 MAM1 ;
  * NODAL FORCES FROM THIS STRESS
  FT = BSIG SIT MOM1 ;
  Linear system solving (additional term to the 2nd member)
  * DISPLACEMENTS CALCULATION BY CALLING SOLVER WITH THERMAL PSEUDO FORCES
  * ADDED TO THE MECHANICAL ONES
  U6 = RESO RITOT (FS ET FV ET FT) ;

## Slide 95: Chap. 6: Linear elasticity THERMAL LOADING
  Post processing: deformed mesh, strains, stresses
  * THERMOMECANICAL DEFORMED MESH
  DEF_6 = (It's up to you)
  DEF_6C = (It's up to you)
  TRAC (It's up to you) ;

## Slide 96: Chap. 6: Linear elasticity THERMAL LOADING
  Post processing: deformed mesh, strains, stresses
  * THERMOMECANICAL DEFORMED MESH
  DEF_6 = DEFO SU U6 150. ;
  DEF_6C = DEFO CSU U6 150. 'ORAN' ;
  TRAC (DEF_INIC ET DEF_5C ET DEF_6C) ;

## Slide 97: Chap. 6: Linear elasticity THERMAL LOADING
  Post processing: deformed mesh, strains, stresses
  * TOTAL STRAINS
  EP = (It's up to you, EPSI operator)
  * ELASTIC STRAINS
  EPE = (It's up to you)
  * STRESSES CALCULATED FROM ELASTIC STRAINS
  SIGT = (It's up to you)
  TRAC SIGT MOM1 DEF_6 CSU ;

## Slide 98: Chap. 6: Linear elasticity THERMAL LOADING
  Post processing: deformed mesh, strains, stresses
  * TOTAL STRAINS
  EP = EPSI MOM1 U6 'LINE' ;
  * ELASTIC STRAINS
  EPE = EP - EPT ;
  * STRESSES CALCULATED FROM ELASTIC STRAINS
  SIGT = ELAS EPE MOM1 MAM1 ;
  TRAC SIGT MOM1 DEF_6 CSU ;

## Slide 99: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Objective: previous thermo-mechanical calculation
  + thermal expansion α variable in space
  calculation of the field α(x) (from coordinates)
  material property described by α(x)
  updating of the nodal thermal pseudo forces
α
x
α0
xmin
xmax
xmean

## Slide 100: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Non uniform thermal expansion coefficient
  XX = COOR SU 1 ;
  XMAX = MAXI XX ;
  XMIN = MINI XX ;
  XMOY = 0.5 * (XMAX + XMIN) ;
  BETA = 7. ;
  CHP_ALPH = ALPHAMAT * (1. + (BETA * (((XX - XMOY) / (XMAX - XMIN)) ** 3))) ;
  Material properties updating
  * CONVERSION FROM CHPOINT -> TO MCHAML
  CHM_ALPH = CHAN 'CHAM' CHP_ALPH MOM1 ;
  * UPDATING OF THE MATERIAL MCHAML WITH THE NON UNIFORM ALPHA
  MAM1B = MATE MOM1 'YOUN' YOUNGMAT 'NU' NUMAT
  'ALPH' CHM_ALPH 'TREF' T0 'TALP' T0 ;

## Slide 101: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Updating the nodal forces due to thermal strains (2nd member)
  * UPDATING THE PURE THERMAL STRAINS WITH ALPHA VARIABLE
  EPT = (It's up to you, EPTH operator)
  * UPDATING THE THERMAL PSEUDO STRESSES WITH ALPHA VARIABLE
  SIT = (It's up to you, ELAS operator)
  * UPDATING THE NODAL FORCES FOR THESE THERMAL STRAINS
  FT = (It's up to you, BSIG operator)
  Linear system solving
  * DISPLACEMENTS WITH ALPHA VARIABLE
  U7 = RESO RITOT (FS ET FV ET FT) ;

## Slide 102: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Updating the nodal forces due to thermal strains (2nd member)
  * UPDATING THE PURE THERMAL STRAINS WITH ALPHA VARIABLE
  EPT = EPTH TFINAL MOM1 MAM1B ;
  * UPDATING THE THERMAL PSEUDO STRESSES WITH ALPHA VARIABLE
  SIT = ELAS EPT MOM1 MAM1B ;
  * UPDATING THE NODAL FORCES FOR THESE THERMAL STRAINS
  FT = BSIG SIT MOM1 ;
  Linear system solving
  * DISPLACEMENTS WITH ALPHA VARIABLE
  U7 = RESO RITOT (FS ET FV ET FT) ;

## Slide 103: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Post processing: deformed mesh, strains, stresses
  * DEFORMED SHAPE WITH ALPHA VARIABLE
  (It's up to you)
  (It's up to you)
  TRAC (It's up to you) ;

## Slide 104: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Post processing: deformed mesh, strains, stresses
  * DEFORMED SHAPE WITH ALPHA VARIABLE
  DEF_7 = DEFO SU U7 150. ;
  DEF_7C = DEFO CSU U7 150. 'ROUG' ;
  TRAC (DEF_INIC ET DEF_6C ET DEF_7C) ;

## Slide 105: Chap. 7: Linear elasticity THERMAL LOADING, non uniform properties
  Post processing: deformed mesh, strains, stresses
  * STRAINS WITH ALPHA VARIABLE
  EP = EPSI U7 MOM1 ;
  * ELASTIC STRAINS WITH ALPHA VARIABLE
  EPE = EP - EPT ;
  * STRESSES WITH ALPHA VARIABLE
  SIGT = ELAS EPE MOM1 MAM1B ;
  TRAC SIGT MOM1 DEF_7 CSU ;

## Slide 106: Chap. 8: Elasto-plastic mechanical analysis THERMAL LOADING, non uniform properties, PASAPAS
  Objective: previous thermo-mechanical calculation
  + perfect elasto-plastic material
  starting from the previous transient thermal analysis
  add a non-linear mechanical model
  temporal description of mechanical loadings
  solving with the PASAPAS procedure
σ
ε
σY
E

## Slide 107: Chap. 8: Elasto-plastic mechanical analysis THERMAL LOADING, non uniform properties , PASAPAS
  Model and material properties updating
  * MECHANICAL MODEL UPDATING
  MOM2 = MODE SU 'MECANIQUE' 'ELASTIQUE' 'PLASTIQUE' 'PARFAIT' ;
  * MATERIAL PROPERTIES UPDATING (YIELD STRENGTH 'SIGY' ADDED TO PROPERTIES)
  MAM2 = MATE MOM2 'YOUN' YOUNGMAT 'NU' NUMAT 'SIGY' SIGYMAT
  'ALPH' CHM_ALPH 'TREF' T0 'TALP ' T0 ;
  Incremental mechanical loading
  * TEMPORAL MECHANICAL LOADS DESCRIPTION
  EVTM = EVOL 'MANU' (PROG 0. (0.98 * TPSFIN) TPSFIN)
  (PROG 0. 0. 1.) ;
  CHAFS = CHAR 'MECA' FS EVTM ;
  CHAFV = CHAR 'MECA' FV EVCTE ;
  CHAM = CHAFS ET CHAFV ;

## Slide 108: Chap. 8: Elasto-plastic mechanical analysis THERMAL LOADING, non uniform properties , PASAPAS
  Building of the table for PASAPAS procedure
  * PASAPAS TABLE
  TAB2 = TABL ;
  ………
  ………
  ………
  (It's up to you)
  ………
  ………
  ………
  PASAPAS TAB2 ;

## Slide 109: Chap. 8: Elasto-plastic mechanical analysis THERMAL LOADING, non uniform properties , PASAPAS
  Building of the table for PASAPAS procedure
  * PASAPAS TABLE
  TAB2 = TABL ;
  TAB2 . 'MODELE' = MOT ET MOC ET MOR ET MOM2 ;
  TAB2 . 'CARACTERISTIQUES' = MAT ET MAC ET MAR ET MAM2 ;
  TAB2 . 'BLOCAGES_MECANIQUES' = BLMX ET BLMY ;
  TAB2 . 'BLOCAGES_THERMIQUES' = BLT ;
  TAB2 . 'CHARGEMENT' = CHAT ET CHAM ;
  TAB2 . 'TEMPS_CALCULES' = PROG 0. 'PAS' (0.02 * TPSFIN) (0.98 * TPSFIN)
  'PAS' (0.001 * TPSFIN) TPSFIN ;
  TAB2 . 'CELSIUS' = VRAI ;
  PASAPAS TAB2 ;

## Slide 110: Chap. 8: Elasto-plastic mechanical analysis THERMAL LOADING, non uniform properties , PASAPAS
  Post-processing: stresses
  * LOOP ON EACH TIME STEP
  LISO2 = PROG 0. 'PAS' 10.E6 100.E6 ;
  N2 = DIME (TAB2 . 'DEPLACEMENTS') ;
  REPE B1 N2 ;
  U_I = TAB2 . 'DEPLACEMENTS' . (&B1 - 1) ;
  DEF_I = DEFO SU U_I 150. ;
  S_I = TAB2 . 'CONTRAINTES' . (&B1 - 1) ;
  TRAC S_I MOM2 DEF_I CSU LISO2 ;
  FIN B1 ;
  DEF_8C = DEFO CSU U_I 150. 'VIOL' ;

## Slide 111: Chap. 8: Elasto-plastic mechanical analysis THERMAL LOADING, non uniform properties , PASAPAS
  Post-processing: cumulated plastic strains (link)
  * LOOP ON EACH TIME STEP
  VI = TAB2 . 'VARIABLES_INTERNES' . (N2 - 1) ;
  EQ_MAX = MAXI (EXCO 'EPSE' VI) ;
  LISO3 = PROG 0. 'PAS' (EQ_MAX / 10.) EQ_MAX ;
  REPE B1 N2 ;
  U_I = TAB2 . 'DEPLACEMENTS' . (&B1 - 1) ;
  DEF_I = DEFO SU U_I 150. ;
  V_I = TAB2 . 'VARIABLES_INTERNES' . (&B1 - 1) ;
  TRAC V_I MOM2 DEF_I CSU LISO3 ;
  FIN B1 ;

## Slide 112: Chap. 9: Elasto-plastic mechanical analysis THERMAL LOADING, variable properties (x,t), PASAPAS
  Objective: previous thermo-mechanical calculation
  + conductivity depending on temperature
  variable material property depending on the thermal unknown
T
210 W.m-1.K-1
250 W.m-1.K-1
50 °C
200 °C

## Slide 113: Chap. 9: Elasto-plastic mechanical analysis THERMAL LOADING, variAblE properties (x,t), PASAPAS
  Updating of material properties
  * VARIATION OF CONDUCTIVITY AS A FUNCTION OF T
  EVLAM = EVOL 'MANU' 'T' (PROG 50. 200.) 'K' (PROG 210. 250.) ;
  * UPDATING OF THE MATERIAL
  MAT2 = MATE MOT 'K' EVLAM 'C' CAPAMAT 'RHO' RHOMAT ;
  PASAPAS call
  (It's up to you)

## Slide 114: Chap. 9: Elasto-plastic mechanical analysis THERMAL LOADING, variable properties (x,t), PASAPAS
  Updating of material properties
  * VARIATION OF CONDUCTIVITY AS A FUNCTION OF T
  EVLAM = EVOL 'MANU' 'T' (PROG 50. 200.) 'K' (PROG 210. 250.) ;
  * UPDATING OF THE MATERIAL
  MAT2 = MATE MOT 'K' EVLAM 'C' CAPAMAT 'RHO' RHOMAT ;
  PASAPAS call
  TAB2 = TABL ;
  TAB2 . 'MODELE' = MOT ET MOC ET MOR ET MOM2 ;
  TAB2 . 'CARACTERISTIQUES' = MAT2 ET MAC ET MAR ET MAM2 ;
  TAB2 . 'BLOCAGES_MECANIQUES' = BLMX ET BLMY ;
  TAB2 . 'BLOCAGES_THERMIQUES' = BLT ;
  TAB2 . 'CHARGEMENT' = CHAT ET CHAM ;
  TAB2 . 'TEMPS_CALCULES' = PROG 0. 'PAS' (0.02 * TPSFIN) (0.98 * TPSFIN)
  'PAS' (0.001 * TPSFIN) TPSFIN ;
  TAB2 . 'CELSIUS' = VRAI ;
  PASAPAS TAB2 ;

## Slide 115: Chap. 9: Elasto-plastic mechanical analysis THERMAL LOADING, variable properties (x,t), PASAPAS
  Post processing: deformed mesh
  * COMPARISON OF THE FINAL SHAPE WITH THOSE OF THE PREVIOUS CALCULATIONS
  N2 = DIME (TAB2 . 'DEPLACEMENTS') ;
  U9 = TAB2 . 'DEPLACEMENTS' . (N2 - 1) ;
  DEF_9 = DEFO SU U9 150. ;
  DEF_9C = DEFO CSU U9 150. 'BLEU' ;
  TRAC (DEF_INIC ET DEF_7C ET DEF_8C ET DEF_9C) ;

## Slide 116: Chap. 9: Elasto-plastic mechanical analysis THERMAL LOADING, variable properties (x,t), PASAPAS
  Post processing: cumulated plastic strains
  VI9 = TAB2 . 'VARIABLES_INTERNES' . (N2 - 1) ;
  EQ_MAX = MAXI (EXCO 'EPSE' VI9) ;
  LISO3 = PROG 0. 'PAS' (EQ_MAX / 10.) EQ_MAX ;
  U9 = TAB2 . 'DEPLACEMENTS' . (N2 - 1) ;
  DEF9 = DEFO SU U9 150. ;
  TRAC VI9 MOM2 DEF9 CSU LISO3 ;

## Slide 117: ADDENDA

## Slide 118: TRUSS, Beam, shell, joint … F.E.
  The choice of the finite elements is made in MODE
    MODP1 = MODE LIG1 'MECANIQUE' 'ELASTIQUE' | 'POUT' | ;
    | 'TIMO' |
    MODC1 = MODE SUR1 'MECANIQUE' 'ELASTIQUE' | 'DKT' | ;
    | 'COQ8' |
  You should give the geometrical characteristics
    MATP1 = MATE MODP1 'YOUN' 210.E9 'NU ' 0.3
    'SECT' 1.E-2 'INRY' 1.E-4 'INRZ' 2.E-4 'TORS' 3.E-4 ;
    MATC1 = MATE MODC1 'YOUN' 210.E9 'NU ' 0.3
    'EPAI' 1.E-2 ;
  Then you can prescribe d.o.f. for displacements and rotation
    BL1 = BLOQ P1 'UX' 'UY' 'UZ' 'RX' 'RY' 'RZ' ;

## Slide 119: Shell elements in 3D
  Example of a cylindrical shell under pressure (in 3D)
    OPTI 'DIME' 3 'ELEM' 'QUA4' ;
    p1 = 4. 0. 0. ;
    lig1 = CERC 45 'ROTA' 360. p1 (0. 0. 0.) (0. 0. 1.) ;
    ELIM lig1 1.E-2 ;
    sur1 = lig1 TRAN 20 (0. 0. 10.) ;
    mo = MODE sur1 'MECANIQUE' 'COQ4' ;
    ma = MATE mo 'YOUN' 210.E9 'NU' 0.3 'EPAI' 0.3 ;
    rig = RIGI mo ma ;
    bl1 = BLOQ 'UX' 'UY' 'UZ' 'RX' 'RY' 'RZ' lig1 ;
    f1 = PRES 'COQU' mo 42.E5 'NORM' ma ;
    u = RESO (rig ET bl1) f1 ;
    def1 = DEFO sur1 u ;
    TRAC 'CACH' def1 ;

## Slide 120: Shell elements in 2D
  The same case (in 2D axisymmetric)
    OPTI 'DIME' 2 'MODE' 'AXIS' 'ELEM' 'SEG2' ;
    p1 = 4. 0. ;
    lig1 = DROI 20 p1 (4. 10.) ;
    mo = MODE lig1 'MECANIQUE' 'COQ2' ;
    ma = MATE mo 'YOUN' 210.E9 'NU' 0.3 'EPAI' 0.3 ;
    rig = RIGI mo ma ;
    bl1 = BLOQ 'UR' 'UZ' 'RT' p1 ;
    f1 = PRES 'COQU' mo -42.E5 'NORM' ;
    u = RESO (rig ET bl1) f1 ;
    def1 = DEFO lig1 u ;
    TRAC def1 ;

## Slide 121: And some other options (1D, 2D AXIS, etc…)
  Example of steady state 2D axisymmetric conduction problem
    OPTI 'DIME' 2 'MODE' 'AXIS' 'ELEM' 'QUA8' ;
    p1 = 10. 0. ;
    p2 = 50. 0. ;
    lig1 = DROI 10 p1 p2 ;
    sur1 = lig1 TRAN 1 (0. 1.) ;
    cot1 = sur1 COTE 4 ;
    cot2 = sur1 COTE 2 ;
    mo = MODE sur1 'THERMIQUE' ;
    ma = MATE mo 'K' 42. ;
    con = COND mo ma ;
    bl1 = BLOQ 'T' cot1 ;
    bl2 = BLOQ 'T' cot2 ;
    f1 = DEPI bl1 20. ;
    f2 = DEPI bl2 500. ;
    t = RESO (con ET bl1 ET bl2) (f1 ET f2) ;
    TRAC t sur1 ;
    evt = EVOL 'CHPO' t 'T' lig1 ;
    DESS evt ;

## Slide 122: And some other options (1D, 2D AXIS, etc…)
  The same case in 1D (cylindrical)
    OPTI 'DIME' 1 'MODE' 'UNID' 'AXIS' 'ELEM' 'SEG3' ;
    p1 = POIN 10. ;
    p2 = POIN 50. ;
    lig1 = DROI 10 p1 p2 ;
    mo = MODE lig1 'THERMIQUE' ;
    ma = MATE mo 'K' 42. ;
    con = COND mo ma ;
    bl1 = BLOQ 'T' p1 ;
    bl2 = BLOQ 'T' p2 ;
    f1 = DEPI bl1 20. ;
    f2 = DEPI bl2 500. ;
    t = RESO (con ET bl1 ET bl2) (f1 ET f2) ;
    TRAC t lig1 ;
    evt = EVOL 'CHPO' t 'T' lig1 ;
    DESS evt ;

## Slide 123: Reading / writing DATA
  Binary file: backup / recovery
    OPTI 'SAUV' 'foo' ; SAUV ;
    OPTI 'REST' 'foo' ; REST ;
    Also possible by a text file
  Run an EXTErnal command
    TAB1 = EXTE 'grep –in mechanical foo.dgibi' 'RC' ;
     TAB1 contents the output of the grep command
  The ACQUisition command
    Read a texte file, line by line
    OPTI 'ACQU' 'foo.txt' ;
    ACQU N1*'ENTIER' A*'FLOTTANT' ;
    ACQU N2*'ENTIER' L1*'LISTREEL' 4 ;
foo.txt
1 3.14 X Y Z
2 25.2 28.3 24.3 16.6

## Slide 124: Reading / writing data
  Writing in a text file
   using the SORT directive
    OPTI 'SORT' 'my_file.txt' ;
    SORT 'CHAI' 'I am writing a text file!' ;
    SORT 'CHAI' 4 8 15 16 23 42 ;
    SORT 'CHAI' ' ' ;
    SORT 'CHAI' '#iteration Fibonacci' ;
    FIBO1 = 0 ;
    FIBO2 = 1 ;
    SORT 'CHAI' 0 FIBO1 ;
    SORT 'CHAI' 1 FIBO2 ;
    REPE B1 15 ;
    FIBO2B = FIBO2 ;
    FIBO2 = FIBO1 + FIBO2 ;
    FIBO1 = FIBO2B ;
    SORT 'CHAI' (&B1 + 1) FIBO2 ;
    FIN B1 ;
foo.txt
I am writing in a text file!
4 8 15 16 23 42
#iteration Fibonacci
0 0
1 1
2 1
3 2
4 3
5 5
6 8
7 13
8 21
9 34
10 55
11 89
12 144
13 233
14 377
15 610
16 987

## Slide 125: Reading / writing data
  LIRE / SORT reading / writing different file formats
    Read/write tabular data (CSV or other)
    concerned objects: lists, TABLE
    used by text editors, spreadsheet (Excel)
    OPTI 'SORT' 'foo.csv' ;
    SORT 'EXCE' OBJECT1 ;
    TAB1 = 'LIRE' 'CSV' 'foo.csv' ;
    The column separator can be changed:
    semicolon, comma, space, tab, slash

## Slide 126: Reading / writing data
  LIRE / SORT reading / writing different file formats
    Read the UNV format (text file)
    concerned objects: MAILLAGE (meshes)
    used by Gmsh, Salomé, HyperMesh, …
    TAB1 = LIRE 'UNV' 'foo.unv' ;
    Read/wrtite the AVS format (text file)
    concerned objects: MAILLAGE, CHPOINT, MCHAML
    .inp extension used by Abaqus
    OPTI 'SORT' 'foo.inp' ;
    SORT 'AVS' OBJET1 'TEMPS' 12.3 ;
    OPTI 'LECT' 'foo.inp' ;
    TAB1 = LIRE 'AVS' ;

## Slide 127: Reading / writing data
  LIRE / SORT reading / writing different file formats
    Write the VTK format
    concerned objects: MAILLAGE, CHPOINT, MCHAML
    used by Paraview
    OPTI 'SORT' 'foo.vtk' ;
    SORT 'VTK' MAIL1 'SCREW' MAIL2 'NUT'
    DEP1 'DISPLACEMENTS' SIG1 'STRESSES' ;

## Slide 128: Reading / writing data
  LIRE / SORT reading / writing different file formats
    Read/write the MED format
    concerned objects: MAILLAGE, CHPOINT, TABLE (from PASAPAS)
    used by Salomé, Europlexus
    OPTI 'SORT' 'foo.med' ;
    SORT 'MED' OBJET1 ;
    TAB1 = LIRE 'MED' 'foo.med' ;
    Read the FEM fomat
    concerned objetcs: MAILLAGE
    used by HyperMesh (Altair)
    TAB1 = LIRE 'FEM' 'foo.fem' ;

## Slide 129: Development: Gibiane procedures
  Concatenate all procedures in a text file with the .procedur extension
  Launch castem22 with the –u option
    castem22 –u
     Cast3M creates a file named UTILPROC (direct access file)
  When Cast3M will be launched all procedures will be available
    The UTILPROC file must be present in the working directory
    Idem for notices (manual pages) (.notice extension files)

## Slide 130: Development: Esope sources
  The user can modify/correct/add the source code of
  operators and directives
  Compilation of Esope source files
    compilcast22 toto.eso
    compilcast22 tata.eso
    ...
  Linking
    essaicast22
     creation of a binary executable file : cast_64_22
     local version of Cast3M
  Can be launched as usual
    castem22 mon_fichier.dgibi

## Slide 131: And to complete
  Peruse documentation regularly
    ~70 instructions reviewed during this course
    Around 1400 available instructions!
  Subscription to the Cast3M mailing list (see the Cast3M web site)
    Send an e-mail at sympa@umontpellier.fr with in the message frame:
    SUB cast3m-util your_name your_firstname
    and nothing more! (no object, no signature, …)
  Club Cast3M: annual users seminar
    Each year in November in the south of Paris
    Presentation of studies performed with Cast3M, developments in the next release
    Free registration!

## Slide 132: Plane linear THERMAL ELASTICITY (1) equations
Total strains (linear)
Strains partition +
Thermal strains
Elasticity
with: displacement total strain stress elastic strain thermal strain identity tensor stiffness tensor (4th order) thermal expansion temperature increment

## Slide 133: Plane linear THERMAL ELASTICITY (2) plane stresses
Plane strains hypothesis:
Vector notation:
Hooke's law:
with:
3 independent components
Hooke matrix

## Slide 134: Plane linear THERMAL ELASTICITY (3) finite elements
Interpolation of primal unknowns:
at each point in the element are the displacements of the element nodes
Case of a TRI3 element (6 dof): Strains (linearized):
A
B
C
with
discrete gradient operator

## Slide 135: Plane linear THERMAL ELASTICITY (4) stiffness matrix
Elementary elastic energy:
Assembly:
finite element "volume"
elementary stiffness matrix (obtained by numerical computation)
nodes displacements (global mesh)
The matrices are extended on all dof with null items
assembly stiffness matrix

## Slide 136: Plane linear THERMAL ELASTICITY (5) principle of virtual work
Principle of virtual work:
prescribed volume forces
prescribed surface forces
nodal equivalent forces

## Slide 137: Plane linear THERMAL ELASTICITY (6) thermal load
We add a second member item:

## Slide 138: Stiffness and Lagrange multipliers
  Mechanics deals with the following constrained problem:
  We have to minimize the following function:
    with the constrain:
  The Lagrange theorem introduces new unknowns so that:
  We have to solve the following linear system:
constraints matrix
imposed values
+

## Slide 139: Stiffness anD Lagrange multipliers
  Example: one bar element
OPTI 'DIME' 2 'ELEM' 'SEG2' ;
* Mesh
p1 = 0. 0. ;
p2 = 3. 0. ;
l1 = DROI 1 p1 p2 ;
* Model and properties
mo = MODE l1 'MECANIQUE' 'BARR' ;
ma = MATE mo 'YOUN' 210.E9 'NU' 0.3
'SECT' 1.E-2 ;
* Main stiffness matrix
rig1 = RIGI mo ma ;
LIST rig1 ;
* Constraint matrix
bl1 = BLOQ 'UX' p1 ;
LIST bl1 ;
* Second member
f1 = DEPI bl1 1.2 ;
LIST f1 ;
lien 1 lien 2
rig1
primal unknowns
matrices
bl1
rig1 ET bl1
dual unknowns

## Slide 140: Accumulated plastic strain
  Definition
  Meaning
    Measure of the length of the flow trajectory in the plastic strain space
  (link)

## Slide 141: Description of Gibiane objects

## Slide 142: objects Description
  General objects
    ENTIER Integer
    FLOTTANT Real
    MOT Characters string
    LOGIQUE Boolean (TRUE and FALSE)
    LISTENTI List of integers
    LISTREEL List of reals
    LISTMOT List of word (restricted to 4 digits)
    TABLE Set of objects of various types characterized by an index of various types
    EVOLUTIO Representation of a function, couple of lists (x ; f(x))

## Slide 143: objects Description
  Objects for meshing
    POINT Coordinates of a point of the space + density
    MAILLAGE Region of the discretized space
  Objects for calculation
    CHPOINT Any data type defined at the mesh nodes (floating, Boolean, fields, …)
    MMODEL Association of a type of finite element and a material behavior with a mesh Defines the primal / dual unknowns ex: displacements / forces
    temperature / heat flux

## Slide 144: objects Description
  Objects for calculation (continuation)
    MCHAML Any data type defined inside the mesh elements (floating, Boolean, fields, …).
    Various supports (Gauss points, center of gravity, nodes, …)
    RIGIDITE Stiffness, mass, conductivity matrix, … Coupling the physical unknowns
    CHARGEME Loading spatio-temporal description
  Objects for post processing
    VECTEUR To visualize multi component fields
    DEFORMEE To visualize a deformed mesh

## Slide 145: DEN/DANS DM2S SEMT
François DI PAOLA
Commissariat à l'énergie atomique et aux énergies alternatives
Centre de Saclay | 91191 Gif-sur-Yvette Cedex
  Etablissement public à caractère industriel et commercial | R.C.S Paris B 775 685 019