## Slide 1
Jason Le Coz(1,2), François Di Paola(1), Guénhaël Le Quilliec(3)
Cast3M annual user’s conference “Club”
November 28, 2025
(1) Université Paris-Saclay, CEA, Service d’Études Mécaniques et Thermiques
(2) Université de Technologie de Compiègne, Laboratoire Roberval
(3) Université de Tours, Laboratoire de Mécanique Gabriel Lamé
An Educational Code for Topological Optimization in Gibiane

## Slide 2
Find the minimum/maximum of a linear/nonlinear function with several variables, with/without constraints (linear/nonlinear)
● Simplex method
SIMP max. of a linear function, with linear equalities/inequalities constraints
● Least Squares method
MOCA min. of the sum of squares distances (observation – prediction)² for a linear function
AJUSTE idem but on a nonlinear function (the iterative scheme is included)
LEVM Levenberg Marquardt method (“damped” least squares)
● Method of Moving Asymptotes (MMA) [1]
Min. of a nonlinear function with nonlinear inequalities
EXCE a variation of the MMA
MMA new “generic” Method of Moving Asymptotes [2]
Approximate the original nonlinear problem with a succession of (simpler) convex problems
I. Optimization operators/procedures in Cast3M
A brief reminder
Must be included in a iterative scheme to deal with nonlinear functions

## Slide 3
● New MMA operator: “generic” Method of Moving Asymptotes [2]
Can handle several “classical” optimization problems:
● KKT_MMA procedure: residuals for the Karush-Kuhn-Tucker conditions
test cases: mma_00.dgibi mma_01.dgibi mma_02.dgibi mma_03.dgibi mma_04.dgibi
Method of Moving Asymptotes (MMA)
(objective function)
(: constraints functions)
( : design variables)
( : slack variables for constraints)
( : regularization variable)
Constrained “standard” min. problem:
s.t.:
Constrained “min-max” problem:
s. t.:
Constrained “least-squares” problem:
s.t.:
I. Optimization operators/procedures in Cast3M
Most used for topological optimization
subject to: for
for
for
_____
new MMA operator:
- uses LISTREELs (instead of TABLEs)
which improves performances
- more generic framework

## Slide 4
● Find the optimal matter distribution in a meshed space to minimize/maximize some properties
optimization variable: continuous element volume fraction (density)
II. Topological Optimization
Introduction to density-based TO
mesh
optimize
design
● Solid Isotropic Material Penalization (SIMP)
Penalize intermediate density contribution to objective or constraint functions
Mechanical application: Young Modulus
● Identify holes for shape/parametric optimization
Airplane structure TO application [3]
HS+
HS-
Hashin-Strickmann criteria

## Slide 5
● Easy to use procedure
Solve the “classical” compliance minimization problem:
II. Topological Optimization
In Cast3M: the TOPOPTIM procedure [4]
eq. to minimize strain energy
subject to: max. global volume fraction
=?
density field
MCHAML object (“element field” on centroids)

## Slide 6
● Easy to use procedure
Solve the “classical” compliance minimization problem:
● Additional features:
● Additional smoothing procedure TOPOSURF
A lot of examples
topoptim_01.dgibi … topoptim_11.dgibi
toposurf_01.dgibi toposurf_03.dgibi
II. Topological Optimization
In Cast3M: the TOPOPTIM procedure [4]
unstructured meshes
2D (plane/axis) 3D models
fixed full/empty zones
multi-case loading
automatic element removal
thermal analysis
nonlinear behavior (plasticity, contact,…)
can be stopped/restarted (remeshing…)
geometric restrictions
eq. to minimize strain energy
subject to: max. global volume fraction
density field
MCHAML object (“element field” on centroids)

## Slide 7
● Transcription in Gibiane of the “88 lines code in Matlab” [5]
● For educational and personal purposes
  + Short, simple, detailed (~280 lines)
  + Easy to modify
  - TOPOPTIM functionalities not available
● Description
Solve the “classical” compliance minimization on MBB:
subject to:
With:
III. The educational codes top_oc.dgibi & top_mma.dgibi
Presentation
Code flowchart
Resolution
Sensitivity analysis
Optimizer
Convergence?
Filter (+ threshold)
Solution
Mesh & Model
SURF, …
MODE ‘MECA’ …
MMA, OC, …
MFIL
MATE, RIGI
RESO …
no
yes
● Sensitivity analysis
Compute

## Slide 8
Some examples!

## Slide 9
● Compliance minimization problem with a non convex object:
Compliance gradient becomes:
● Test case: hanging bar (punctual force + gravity)
Example of design-dependent loads (gravity, centrifugal forces, Laplace forces,…)
IV. Nonconvex problems
=?

## Slide 10
● Compliance minimization problem with a non convex object:
Compliance gradient becomes:
● Test case: hanging bar (punctual force + gravity)
Example of design-dependent loads (gravity, centrifugal forces, Laplace forces,…)
IV. Nonconvex problems
Good agreement with the reference analytical solution [6]

## Slide 11
● Compliance minimization problem with a non convex object:
Compliance gradient becomes:
● Test case: hanging bar (punctual force + gravity)
● Test case: arch bridge (gravity only!)
Example of design-dependent loads (gravity, centrifugal forces, Laplace forces,…)
IV. Nonconvex problems
=?

## Slide 12
● Compliance minimization problem with a non convex object:
Compliance gradient becomes:
● Test case: hanging bar (punctual force + gravity)
● Test case: arch bridge (gravity only!)
Solution may depend on the starting point
and be only a local minimum!
Example of design-dependent loads (gravity, centrifugal forces, Laplace forces,…)
IV. Nonconvex problems

## Slide 13
● From the compliance minimization problem:
● Measure of the “local” (neighboring) volume fraction
● Local constraints  aggregated into a single differentiable constraint
Example of “infill” optimization for additive manufacturing [7]
IV. Multi-constrained problem
subject to: max. global volume fraction
?
where
 
max. local volume fraction
centroid
distance
P-mean function: soft max.
AGRE operator
Linear filter
MFIL operator
Optimal topology with

## Slide 14
● From the compliance minimization problem:
● Measure of the “local” (neighboring) volume fraction
● Local constraints  aggregated into a single differentiable constraint
Example of “infill” optimization for additive manufacturing [7]
IV. Multi-constrained problem
where
 
max. local volume fraction
centroid
distance
P-mean function: soft max.
AGRE operator
Linear filter
MFIL operator
Optimal topology with
Optimal topology with and
subject to: max. global volume fraction

## Slide 15
● Robustness (to damage)
Let’s introduce a damaged zone in the structure
What’s the effect on the compliance (objective function)?
Example of “infill” optimization for additive manufacturing [7]
IV. Multi-constrained problem
Optimal topology with
Optimal topology with and

## Slide 16
● Robustness (to damage)
Let’s introduce a damaged zone in the structure
What’s the effect on the compliance (objective function)?
● Robustness (to load uncertainty)
Example of “infill” optimization for additive manufacturing [7]
IV. Multi-constrained problem
Optimal topology with
Optimal topology with and
Without infill constraint
With infill constraint
Without infill constraint
With infill constraint

## Slide 17
● Maximize structure displacement according to a load/displacement input
Case of compliant mechanism [8]
IV. Adjoint problem
● Optimization problem:
subject to:
with:

## Slide 18
● Maximize structure displacement according to a load/displacement input
Case of compliant mechanism [8]
IV. Adjoint problem
● Optimization problem:
subject to:
with:
● Adjoint problem:
Adjoint system:

## Slide 19
● Maximize structure displacement according to a load/displacement input
Case of compliant mechanism [8]
IV. Adjoint problem
● Optimization problem:
subject to:
with:
small disp. ≢ large disp.
● Adjoint problem:
Adjoint system:

## Slide 20
● Available here (for Cast3M version 2026):
top_oc.dgibi top_mma.dgibi
● New simple Gibiane test cases for topological optimization (T.O.)
Easy to read and adapt to many T.O. problems
Examples of application to non-convex/multi-constrained T.O. problems
Extension to other objective/constraints functions
“Sandbox” for testing new formulations
● Coming soon:
GC MMA (Globally Convergent)
Other examples: stress-based T.O., multi-physics (thermo-mechanical, …) T.O.
Implementation in the TOPOPTIM procedure (for the most common problems)
Conclusion and perspectives

## Slide 21
[1] K. Svanberg The method of moving asymptotes – a new method for structural optimization International Journal for Numerical Methods in Engineering, 24, 359-373 (1987)
[2] K. Svanberg MMA and GCMMA – two methods for nonlinear optimization (2017) https://people.kth.se/~krille/mmagcmma.pdf
[3] L. A. Krog, L. A. Tucker, G. Rollema
Application of Topology, Sizing and Shape Optimization Methods to Optimal Design of Aircraft Components
https://api.semanticscholar.org/CorpusID:11846281
[4] G. Le Quilliec Procédure d'optimisation topologique TOPOPTIM Version 2 Club Cast3M (2017)
[5] E. Andreassen, A. Clausen, M. Schevenels, B. S. Lazarov, O. Sigmund Efficient topology optimization in MATLAB using 88 lines of code
Structural and Multidisciplinary Optimization, vol. 43 (2011)
References

## Slide 22
[6] B. L. Karihaloo, W. S. Hemp
Maximum strength/stiffness design of structural members in presence of self-weight
Proceedings of the Royal Society, A 389, 119-32 (1983)
[7] J. Wu, N. Aage, R. Westermann, O. Sigmund Infill Optimization for Additive Manufacturing – Approaching Bone-like Porous Structures
IEEE Transactions on Visualization and Computer Graphics 24(2):1127--1140 (2018)
[8] C.B.W. Pedersen, T. Buhl, O. Sigmund Topology synthesis of large-displacement compliant mechanisms
Int. J. Numer. Meth. Engng., 50: 2683-2705 (2001)
References